[Total No. of Questions: 09]		[Total No. of Pages: ]
Uni. Roll No. …......................
Program/Course: B. Tech.
Subject: Design of Concrete Structures - II
Subject Code: CE–310
Paper ID: A0622
Time Allowed: 03 Hours		Max. Marks: 60

Note:
1. Section – A is compulsory.
2. Attempt any four questions from Section – B.
3. Attempt any two questions from Section – C.
4. Use of Indian Standards is allowed.
5. Any missing data may be assumed appropriately
		Section – A
Q 1.		Sketch correct way of reinforcement (horizontal) detailing at the junction of vertical walls of rectangular water tank.	2
		How will you decide minimum reinforcement in case of water tank?	2
		Under what conditions, you will recommend Raft Foundation?	2
		Why Shell Structures are structurally more efficient and require less material.	2
		Write, in brief, the procedure to design staging of OHSR.	2
		Sketch detail of Flexible Joint between vertical wall and base slab of a circular water tank.	2
		Discuss the loadings, which a designer has to consider for the design of vertical wall of rectangular underground tank.	2
		Sketch “Strap Footing”, write conditions under which this type footing is the best solution.	2
		What is the role of Shear Key in the “Retaining wall”? On what basis it is designed?	2
		How design of water retaining structures differ from other reinforced structures?	2
		Section – B
Q 2.		How one way and two way shear is calculated in case of isolated square footing of uniform thickness.	5
Q 3.		Write situations where designer has to go for beam curved in plan. How design of such beam differ from the design of straight beam?	5
Q 4.		Derive expressions for meridional and hoop stresses for a Spherical Dome subjected to u.d.l.	5
Q 5.		Show deflected shape of all components of Intze Tank Proper due to membrane action.	5
Q 6.		Under what circumstances Counterfort Retaining Wall is preferred over Cantilever Retaining Wall. Sketch Counterfort Retaining Wall, and label its various components.	5
		Section – C
Q 7.		Design a combined rectangular footing for two columns carrying axial loads of 1000 kN and 1200 kN. Columns are of size 400 mm x 400 mm and are spaced 4 m c/c. The projection of footing from the centre of lightly loaded column is 500 mm. The safe bearing capacity of soil is 120 kN / m2 . Use M20 grade of concrete and Fe–415 grade of steel.	10
Q 8.		Design of cantilever retaining wall to maintain a level difference of 3 m. The angle of repose of earth %iPHI = 30 ^ %omicron, density is 18 kN / m3, coefficient of friction ( between concrete and soil ) %mu = 0.55. Take safe bearing capacity of soil as 100 kN / m2.	10
Q 9.		Design a water tank using approximate method, circular in plan, with internal diameter 6 m, water height of 2.5 m. Take M20 concrete, Fe–415 steel, free board of 200 mm. The tank is resting on ground, the joint between wall and slab is monolithic.	10

###########