[Total No. of Questions: 09]		[Total No. of Pages: ]
Uni. Roll No. …......................
Program/Course: B. Tech. (Sem. 6th)
Subject: Design of Concrete Structures - II
Subject Code: CE–310
Paper ID: A0622
Time Allowed: 03 Hours		Max. Marks: 60

Note:

1. Section – A is compulsory.
2. Attempt any four questions from Section – B, any two questions from Section – C.
3. Use of Indian Standards is allowed.
4. Use M20 concrete and Fe 415 reinforcement.
5. Any missing data may be assumed appropriately

		Section – A
Q 1.		Tabulate development length required for following combination of materials: / 1) M20 and Fe 415 / 2) M30 and Fe 500 / for both tension and compression cases.	2
		Draw shape of bending moment and shear force for a strap beam of a strap footing.	2
		Find hoop force in a ring beam of size 300 mm x 200 mm. The meridian force of 50 kN / m transferred by dome at an angle 30O measured with respect to horizontal.	2
		Under what circumstances, raft footing is recommended?	2
		How circular footing is designed for circular columns?	2
		How torsion is takes care, in case of beams curved in plan?	2
		Sketch Intze tank, and label its all structural components.	2
		Why shells have relatively smaller thickness?	2
		Draw shape of shear force and bending moment for a trapezoidal footing.	2
		What type of stresses are induced in conical dome due to self weight?	2
		Section – B
Q 2.		Design stem of a counterfort retaining wall, which is 7 m high above the top of base slab. Retained soil has unit weight 16 kN / m3, angle of repose is 30O. The counterforts are 300 mm thick and are spaced at 3.5 m c/c.	5
Q 3.		Design footing for a column of size 300 x 300, loaded with a load of 250 kN. The safe bearing capacity of soil is 150 kN / m2.	5
Q 4.		Design a circular water tank, resting on ground, to have water height of 3 m. Take internal diameter as 4 m.	5
Q 5.		Derive expression for membrane stresses for a spherical dome subjected to uniformly distributed load.	5
Q 6.		Design dome for a circular hall. The diameter of hall is 20 m, and dome is subjected to imposed load of 1.0 kN/ m2.	5
		Section – C
Q 7.		Design base slab of a cantilever retaining wall, to retain 3.2 m height of level soil having unit weight 16 kN / m3, angle of repose is 30O. Take 1.2 m depth of footing, where safe bearing capacity of soil is 150 kN / m2.	10
Q 8.		Design a rectangular footing, 6 m long to support two columns of size 450 mm x 450 mm, spaced 4 m c/c. Each column transfers a load of 1250 kN. The safe bearing capacity of soil is 120 kN / m2.	10
Q 9.		Find coefficients for bending moment and shear force at salient point of a ring beam supported on 6 columns, when it is loading by uniformly distributed load.	10

************