# Civil Engineering Department
## Guru Nanak Dev Engineering College, Ludhiana
1st House Test
M.Tech 1st	MTST-502 Bridge Engineering

Date: Sat 21 Feb 15	Time: 10:30 a.m. to 12:00 noon	Max. Marks 30

Don't write anything on question paper except your Roll No. _____________

1	Sketch components of a slab type bridge to be constructed over a drain; Write down purpose / function of each component.	10
2	For a decision to be taken by an Engineer for the site for a bridge and appropriate bridge type, what type of information / data he needed? How required data is collected?	10
3(a)	Write in detail traffic requirements of Highway Bridges.	10
	or
3(b)	What do you understand by waterway of a bridge, and how it is calculated. What will be linear waterway required for a bridge to be constructed across the river, having catchment area 600 hectares, 10 mm per hour is the maximum rainfall intensity, 1.2 m/s is the permissible velocity, 1.8 m is the average depth of flow. Take runoff coefficient as 0.60.	10