[Total No. of Questions: 08]		[Total No. of Pages: ]
Uni. Roll No. …......................
Program/Course: M. Tech.
Subject: Computer Aided Design Methods
Subject Code: CE–507
Paper ID: E0854
Time Allowed: 03 Hours		Max. Marks: 100

Note:
1. Attempt any five questions.
2. Any missing data may be assumed appropriately
Q1.	a)	What are the roles played by the designer and computer in a Computer Aided Design process?	12
	b)	Name various devices required for a CAD office, and clearly explain the function of each device.	8
Q2.	a)	How images are displayed on monitors?	5
	b)	Tabulate coordinates of pixels, which needed to draw a circle of diameter 10 units with center at (10,7) of a given raster display of 20x14 resolution (making use of a graph paper supplied) and draw it on graph paper. Name the algorithm used.	15
Q3.	a)	What do you understand by Flow Chart, how it help in automating analysis / design task with the help of computers?	8
	b)	Write short notes on: / Translation of graphic entities / Clipping in graphic windows	12
Q4.		Explain various techniques to represent 3-D objects in Computers? What do you understand by hidden surface elimination, and how it is achieved?	20
Q5.	a)	How raster graphics differ from vector graphics. Discuss their application and suitability.	5
	b)	Discuss 5 input devices (of a Graphics Workstation) with their advantages and limitations.	15
Q6.	a)	Write down steps (or draw flow chart) to calculate design shear stress for concrete mix ranging from M15 to M 60 (with interval of 5), and percentage steel ranging from 0.1 to 4.0 (with interval of 0.05). The design shear stress is given by: / {%tau}_{v} = {0.85 sqrt{0.8 f_{ck}} (sqrt{1 + 5 %beta} - 1)} over {6 %beta} where %beta = {0.8 f_ck} over {6.89 p_t} / %beta can not less than 1. P_{t} = {100 A_s} over {b_w d}	10
	b)	Write a computer program for the shear stress calculation, as required in Q6 (a).	10
Q7.		Explain the procedure to formulate stiffness matrix for a 2D frame member in member coordinate system, and then to transfer the same to global coordinate system. Write a pseudo code for the same.	20
Q8.		What are various types of Data Base Management Systems. Discuss their structure, relative advantages and disadvantages. How data is stores and retrieved?	20

###########